## Slide 1: SC-PTM Introduction
2015.12

## Slide 2: Background
SC-PTM：Single cell point to multipoint transmission mode over the radio interface to transfer MBMS session data over a single cell using the PDSCH.
To support Dynamic Multicast, such as Mission Critical PTT (public safety), top videos/ popular apps download, mobile advertising, etc
The WI focuses on the radio efficiency improvement for these MBMS service.
Up to now, the SI and the WI (core part) are finished.
Study Item
WI(core part)
WI(performance part)
2015/1
2015/6
2015/12
2016/6

## Slide 3: Benefits
 | SC-PTM | MBSFN
Broadcast area | Dynamic | Static (not adapted to different UE distribution and UE mobility)
Scheduling and resource allocation | SC-PTM transmission and unicast transmission could be multiplexed in the same subframe | Occupy the whole subframe (not adapted to different traffic data, lead to waste or congestion)
Cyclic prefix | supports normal cp and extended cp | only support extended cp (lead to 14.3% system capacity lost)
Network deployment | Easy, Dynamic scheduling | Use pre-established MBMS Point to Multipoint Radio Bearer to reduce the Latency

## Slide 4: Architecture
SC-PTM transmission is assumed to be another bearer type for MBMS transmission (in addition to MBSFN transmission), so the Rel-12 MBMS architecture is used, and the Rel-12 GCSE architecture is also used.

## Slide 5: High level procedure
When the GCS AS wishes to activate an MBMS bearer over MB2, a CELL List is sent to all MBMD nodes.
MCE is the node to make the decision on whether to use SC-PTM or MBSFN.

## Slide 6: RAN1 Aspect
RAN decides
HARQ operation is not supported for SC-MCCH.
HARQ operation is not supported for SC-MTCH.
The concept of transmission mode does not apply to the SC-PTM transmission
The existing CSS is used to transmit the DCI for SC-PTM transmission and therefore does not intend to develop an additional search space for SC-PTM
In order to support SC-PCM, the chipset only needs the software update.

## Slide 7: Channel mapping
Single-Cell Multicast Control Channel (SC-MCCH) ;
Single-Cell Multicast Traffic Channel (SC-MTCH);
SC-RNTI: Identifies transmissions of the SC-MCCH.
G-RNTI: Identifies transmissions of a SC-MTCH

## Slide 8: Single-cell transmission
there is one SC-MCCH per cell;
The value of the SC-RNTI is predefined in the specification
one-to-one mapping between TMGI and G-RNTI;
SC-MCCH and SC-MTCH transmissions are each indicated by a logical channel specific RNTI on PDCCH
the SC-MCCH provides the list of all MBMS services with ongoing sessions transmitted on SC-MTCH(s), including for each MBMS service TMGI and optional session ID, associated G-RNTI and scheduling information
SIB 20: MCCH configuration
PDCCH (SC-RNT,G-RNTI)
PDSCH: SC-MCCH(SC-PTM configuration ), SC-MTCH

## Slide 9: Mobility
For each MBMS service provided using SC-PTM, E-UTRAN indicates in the SC-MCCH the list of neighbour cells providing this MBMS service using SC-PTM.
UE can request unicast reception of the service before changing to a cell not providing the MBMS service using SC-PTM.
UE can continue SC-PTM reception of the service when changing to a cell providing the MBMS service using SC-PTM.